## Slide 1: LECTURE ID :18B11CS311STL02 PROGRAMME : B.Tech. COURSE TITLE : Computer Networks and Internet of Things LECTURE TITLE : Routing Principle (Part I) FACULTY NAME : Dr. Shobhit Tyagi

## Slide 2: Routing Principle (Part I)
By Dr. Shobhit Tyagi Dept. of CSE & IT JIIT, NOIDA

## Slide 3: Topics of Today’s Lecture
Network Layer Service
Datagram and VC Services
IP Datagram Format
Datagram Encapsulation and Fragmentation

## Slide 4
The Network layer is the third layer in the OSI model of computer networks. Its main function is to transfer network packets from the source to the destination.
It is involved both at the source and the destination. At the source, it accepts a packet from the Transport layer, encapsulates it in a datagram, and then delivers the packet to the Data link layer for further transmission to the receiver.
At the destination, the datagram is decapsulated, the packet is extracted, and it is delivered to the corresponding Transport layer.
Network Layer Service

## Slide 5
The services which are offered by the network layer protocol are as follows –
Packetizing:
Packetizing is the process of encapsulating data received from upper layers (also known as the payload) into a Network layer packet at the source and decapsulating the payload from the Network layer packet at the destination.
At the source, the Network layer adds a header containing the source and destination addresses, along with other relevant information required by the Network layer protocol. This packet is then delivered to the Data Link layer for further transmission.
Network Layer Service

## Slide 6
Routing and Forwarding:
These are two additional services provided by the Network layer. In a network, multiple routes may be available from the source to the destination.
The Network layer employs various strategies to determine the best possible route.
This process is known as routing. Several routing protocols facilitate this process, helping routers coordinate with each other and establish communication throughout the network.
Network Layer Service

## Slide 7
Routing and Forwarding:
Forwarding is defined as the action taken by each router when a packet arrives at one of its interfaces.
When a router receives a packet from one of its attached networks, it must forward the packet to another attached network (in the case of unicast routing) or to multiple attached networks (in the case of multicast routing).
Network Layer Service

## Slide 8
Advantages of Network Layer Services:
The packetization service in the Network layer facilitates the efficient transportation of data packets.
Packetization helps eliminate single points of failure in data communication systems.
Routers in the Network layer reduce network traffic by creating separate collision and broadcast domains.
Through forwarding, data packets are effectively transferred from one location to another within the network.
Network Layer Service

## Slide 9
Datagram and VC Services
Both Virtual Circuits and Datagram Networks are types of connection services used for transmitting information from a sender to a receiver.
The primary difference between the two is that Virtual Circuits are connection-oriented services requiring resources such as buffers, CPU, and bandwidth for a data transfer session. In contrast, Datagram Networks are connectionless services that do not require such resources for data transmission.

## Slide 10
What are Virtual Circuits?
A Virtual Circuit is a connection-oriented service where resources such as buffers, CPU time, and bandwidth are allocated to create a dedicated data transfer session. This type of service is also known as connection-oriented switching.
In a virtual circuit, the path taken by the first data packet is established and fixed, so all subsequent packets follow the same path and use the same resources. As a result, all packets in the same session use a consistent header.
Datagram and VC Services

## Slide 11
What are Virtual Circuits?
Due to these characteristics, virtual circuits are generally less complex and more reliable for data transmission. However, they can be expensive to install and maintain. Virtual circuits are commonly used in Asynchronous Transfer Mode (ATM) networks, which are often employed for telephone calls.
Datagram and VC Services

## Slide 12
Datagram and VC Services
What are Virtual Circuits?
Sender
Data Transfer
Call Request
Clear
ack
Call Accept
Nodes
Receiver
A
1
2
B

## Slide 13
What are Datagram Networks?
Datagram networks are connectionless services for data transmission, where resources such as CPU time, buffers, and bandwidth are not reserved in advance.
In datagram networks, the path for data transmission is not predetermined. Instead, data packets can take different routes to their destination, which each packet potentially following a different path based on the current state of the routing tables in intermediate routers. This dynamic routing allows packets to be directed independently through the network.
Datagram and VC Services

## Slide 14
What are Datagram Networks?
Since data packets can follow different paths, each packet may have a distinct header with information specific to that packet.
Due to dynamic resource allocation and variable routing paths, datagram networks are more prone to errors and less reliable compared to connection-oriented networks.
However, datagram networks are cheaper to install and maintain. They are widely used in IP (Internet Protocol) services, such as the internet.
Datagram and VC Services

## Slide 15
Datagram and VC Services
Datagram Packets
Router
Datagram
Packets
B
A
A
A
A
B
B
D
D
D
D
C
C
C
Host 1
C
A
B
D
Host 2
C
A
B
D
What are Datagram Networks?

## Slide 16
IP Datagram Format
Format of an IP Datagram:
An IP datagram is the format of data that can be recognized and processed by the IP protocol. It consists of two components; the header and the data.
The fields within the datagram, excluding the data itself, each have specific roles in the data transmission process.
Every field in the IP datagram has a fixed size, except for the IP Options field, which can range from 20 to 60 bytes in length. The header is used by the sending computer to communicate with the protocol at the same layer on the destination computer.

## Slide 17
Format of an IP Datagram:
IP Datagram Format
32 bits = 4 bytes
Null bit
Don't fragment
More fragment
Version 4 bits
HLEN 4 bits
Type of
Service 8 bits
Total Length 16 bits
Identification 16 bits
0
1 bits
DF
1 bits
DF
1 bits
Fragment Offset
13 bits
Time to Leave 8 bits
Protocol 8 bits
Header Checksum 16 bits
Source IP 32 bits
Destination IP 32 bits
Option 0 to 40 bytes
DATA
32 bits
DATA = 20 bytes to 65,536 bytes
Maximum
Header = 60 bytes
Minimum
Header = 20 в
20 bytes
4 bytes
4 bytes
4 bytes
4 bytes

## Slide 18
VERSION: Version of the IP protocol (4 bits), which is 4 for IPv4.
HLEN: IP header length (4 bits), indicating the number of 32-bit words in the header. The minimum value for this field is 5 and the maximum is 15.
Type of Service: Specifies Low Delay, High Throughput, and Reliability (8 bits).
Total Length: Length of the header plus data (16 bits). The minimum value is 20 bytes, and the maximum is 65,535 bytes.
IP Datagram Format

## Slide 19
Identification: Unique packet ID for identifying the fragments of a single IP datagram (16 bits).
Flags: Three 1-bit flags: reserved bit (must be zero), do not fragment flag, and more fragments flag (to indicate if there are more fragments).
Fragment Offset: Represents the number of data bytes ahead of a particular fragment within the datagram. It is specified in units of 8 bytes, with a maximum value of 65,528 bytes.
Time to Live (TTL): Indicates the datagram’s lifetime (8 bits). It prevents the datagram from looping indefinitely through the network by limiting the number of hops (i.e., the number of routers it can pass through) before being delivered to the destination.
IP Datagram Format

## Slide 20
Protocol: Specifies the protocol to which the data should be passed (8 bits).
Header Checksum: A 16-bit checksum used to detect errors in the datagram header.
Source IP Address: The 32-bit IP address of the sender.
Destination IP Address: The 32-bit IP address of the receiver.
Options: Optional fields that may include information such as source route or record route. These are used by network administrators for various purposes, such as checking whether a path is functioning correctly.
IP Datagram Format

## Slide 21
Data Encapsulation :
Encapsulation is the process of adding additional information to data as it travels through the OSI or TCP/ IP model. This additional information is added on the sender’s side, starting from the Application layer and progressing down to the Physical layer.
Datagram Encapsulation and Fragmentation

## Slide 22
Working of Encapsulation :
No additional information is added to the user’s data in the Application layer of the TCP/ IP model or in the Application, Presentation, Session layers of the OSI model.
The Session layer then passes the data to the Transport layer.
In the Transport layer, the data is divided into smaller pieces. Each piece is encapsulated with a header containing information such as source port, destination port, sequence number, etc. The result is a new form of data that combines the original data with the headers.
The encapsulated data in the Transport layer is referred to as Segments or Datagrams. If TCP is used for transmission, it is called Segments; if UDP is used, it is called Datagrams.
Datagram Encapsulation and Fragmentation

## Slide 23
Now, the data travels down to the Network layer, where a Layer 3 header is added. This header contains information such as source IP address, destination IP address, and other relevant details. The result is a new form of encapsulated data. At this stage, the encapsulated data in the Network layer is referred to as Packets
Datagram Encapsulation and Fragmentation
Data
L4 Header

## Slide 24
The network layer then sends the packet to the Data Link layer. Upon entering the Data Link layer, a new header (Layer 2) is added, along with a trailer. The header includes information such as the source and destination MAC addresses, while the trailer is used for error checking. The encapsulated data in the Data Link layer is referred to as Frames.
Datagram Encapsulation and Fragmentation
Data
L4 Header
L3 Header

## Slide 25
The physical layer receives frames from the Data Link layer. At this stage, the data is encapsulated into a format called Bits. This process illustrates how encapsulation occurs throughout the layers of the OSI or TCP/ IP models.
Datagram Encapsulation and Fragmentation
L2 Trailer
Data
L4 Header
L3 Header
L2 Header

## Slide 26
Protocol Data Unit (PDU) :
The encapsulated data is referred to by different names as it moves through each layer of the OSI or TCP/IP model. These names are collectively known as Protocol Data Units (PDUs). The following table shows the name of the encapsulated data at each layer.
Datagram Encapsulation and Fragmentation
Data
Presentation
Data
Application
Data
Session
Segments/Datagrams
Transport
Packets
Network
Frames
Data Link
Bits
Physical

## Slide 27
De-encapsulation :
De-encapsulation is the reverse process of encapsulation. The additional information added on the sender’s side (during encapsulation) is removed as the data travels from the Physical layer to the Application layer on the receiver’s side.
Datagram Encapsulation and Fragmentation

## Slide 28
Datagram Encapsulation and Fragmentation
Application
Presentation
Session
Transport
Network
Data Link
Physical
SENDER
Data
Bits
Receiver
Application
Presentation
Session
Transport
Network
Data Link
Physical
De-encapsulation
Encapsulation
L4 Header Data
L3 Header L4 Header Data
L2 Header
L3 Header
L4 Header
Data
L2 Trailer

## Slide 29
Fragmentation:
Fragmentation occurs at the Network layer when the size of datagram exceeds the maximum size that can be accommodated by a frame, known as the Maximum Transmission Unit (MTU). To ensure data flow is not disrupted, the Network layer divides the datagram received from the Transport layer into smaller fragments.
Since the IP header has a 16-bit field for total length, the maximum size of an IP datagram = 216 – 1 = 65, 535 bytes.
Fragmentation is performed by the Network layer and typically occurs at routers along the path to the destination.
Datagram Encapsulation and Fragmentation

## Slide 30
IP Fragmentation:
IP Fragmentation is the process of dividing a datagram into smaller fragments during transmission.
This process is performed by intermediary devices, such as routers, or by the destination host at the Network layer.
Datagram Encapsulation and Fragmentation

## Slide 31
Need for IP Fragmentation:
Each network has a Maximum Transmission Unit (MTU), which dictates the maximum size of the packet that can be transmitted through it.
Data packets larger than MTU cannot be transmitted through the network.
Therefore, datagrams are divided into fragments that are smaller than or equal to the MTU.
This ensures that data packets can be transmitted efficiently across networks with varying MTU sizes.
Datagram Encapsulation and Fragmentation

## Slide 32
Datagram Fragmentation:
When a router receives a datagram for further transmission, it examines the following:
The size of the datagram.
The MTU of the destination network.
The value of the DF (Don’t Fragment) bit in the IP header.
Datagram Encapsulation and Fragmentation

## Slide 33
Then, the following cases are possible:
Case 1:
If the size of the datagram is smaller than or equal to the MTU
The router transmits the datagram without fragmentation.
Case 2:
If the size of the datagram is greater than the MTU and the DF (Don’t Fragment) bit is set to 1
The router discards the datagram.
Datagram Encapsulation and Fragmentation

## Slide 34
Case 3:
If the size of the datagram is greater than the MTU and the DF (Don’t Fragment) bit is set to 0.
The router divides the datagram into fragments of size less than or equal to the MTU.
The router attaches an IP header to each fragment, making the necessary adjustments.
The router then transmits all the fragments of the datagram.
Datagram Encapsulation and Fragmentation

## Slide 35
Datagram Encapsulation and Fragmentation
176 B
20 B
Received Datagram
(Second Fragment From Router -1)
88 B
20 B
88 B
20 B
1st
2nd
Fragments of Received Datagram

## Slide 36
Datagram Encapsulation and Fragmentation
176 B
20 B
1st
Fragments Received by Receiver
2nd
88 B
20 B
3rd
88 B
20 B
4th
148 B
20 B

## Slide 37
Thank You