## Slide 1
LECTURE : 18B11CS311PML02
PROGRAMME : B.Tech.
COURSE TITLE : Computer Network and IoT
LECTURE TITLE : Network Models, Protocol and their Services
FACULTY NAME : Mr. Pankaj Mishra

## Slide 2
By
Mr. Pankaj Mishra Dept. of CSE & IT JIIT, NOIDA
Network Models, Protocol and their Services

## Slide 3
Why Layering ?
OSI Model
TCP/IP Protocol Suite Model
Topics of Today’s Lecture

## Slide 4
Why Layering ?
Networks are complex!
A network is a combination of hardware and software that sends dat from one location to another. The hardware consists of the physical equipment that carries signals from one point of the network to another. The software consists of instruction sets that make possible the services that we expect from a network.
many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software

## Slide 5
Layering of Postal Mail

## Slide 6
At the Sellder Site
Let us first describe, in order, the activities that take place at the sender site.
o Higher layer. The sender writes the letter, inserts the letter in an envelope, writes the sender and receiver addresses, and drops the letter in a mailbox.
o Middle layer. The letter is picked up by a letter carrier and delivered to the post office.
o Lower layer. The letter is sorted at the post office; a carrier transports the letter.
At the Receiver Site
o Lower layer. The carrier transports the letter to the post office.
o Middle layer. The letter is sorted and delivered to the recipient's mailbox.
o Higher layer. The receiver picks up the letter, opens the envelope, and reads it.

## Slide 7: Layering
Layering:-A technique to organize a network system into a succession of logically distinct entities, such that the service provided by one entity is solely based on the service provided by the previous (lower level) entity
Advantages
  Modularity – protocols easier to manage and maintain
  Abstract functionality –lower layers can be changed without affecting the upper layers
  Reuse – upper layers can reuse the functionality provided by lower layers
Disadvantages
  Information hiding – inefficient implementations
Unit-1
1-

## Slide 8: Network Models/Standardized Protocol Architectures
Required for devices to communicate
Two standards:
  OSI Reference model
  TCP/IP protocol suite
    Most widely used
Unit-1

## Slide 9: OSI - The Model
Open Systems Interconnection (OSI) is a layered model
Developed by the International Organization for Standardization (ISO)
A theoretical system delivered too late! and has Seven layers
Each layer performs a subset of the required communication functions
Each layer relies on the next lower layer to perform more primitive functions
Each layer provides services to the next higher layer
Changes in one layer should not require changes in other layers
Unit-1

## Slide 10: ISO OSI Reference Model
Seven layers
  Lower three layers are peer-to-peer
  Next four layers are end-to-end
Unit-1
1-
Application
Presentation
Session
Transport
Network
Datalink
Physical
Application
Presentation
Session
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Physical medium

## Slide 11
Physical
  Physical interface between devices
    Mechanical (joins 1 or more signal conductor, circuits)
    Electrical (Representation of bits and bit rate)
    Functional ( function performed by individual circuits )
    Procedural (sequence of events)
  Modulation and Demodulation
  Raw bit stream
  Modem: broadly used to refer to any module that performs the function above
Unit-1

## Slide 12
Data Link Layer
  Means of activating, maintaining and deactivating
  a reliable link
  Segmenting mechanism
  Framing (Header and Trailer)
  Error detection
  Data synchronization( b/w transmitter and receiver)
  Flow control
  Error Control
  Higher layers may assume error free transmission
Unit-1

## Slide 13
Network Layer
  Transport of information
  Virtual circuit service (connection oriented)
  Packet switching or datagram service (connection less)
  Logical addressing (IP address)
  Routing
  Congestion control (flow of packet into the network)
  Both connection-less and connection-oriented
Unit-1

## Slide 14
Transport
  Exchange of data between end systems
  Error free
  In sequence (segment)
  No losses
  No duplicates
  Quality of service( Throughput, transit delay, error rate)
Unit-1

## Slide 15
Session
  Control of dialogues between applications/Dialogue discipline
  Grouping
  Synchronization/check points
  Recovery
Presentation
  Data formats
  Architecture specific (Big-endian or Little-endian)
  Provide conversion from one encoding schema to another encoding schema
  Data compression
  Encryption
Application
  Means for applications to access OSI environment
  E mail, web browsers,
Unit-1

## Slide 16: TCP/IP Protocol Architecture
Developed by the US Defense Advanced Research Project Agency (DARPA) for its packet switched network Advanced Research Projects Agency Network (ARPANET)
Used by the global Internet
No official model but a working one.
  Application layer
  Host to host or transport layer
  Internet layer
  Data link / Network access layer
  Physical layer
Unit-1

## Slide 17: Physical Layer
Similar to OSI model physical layer
Physical interface between data transmission device (e.g. computer) and transmission medium or network
Characteristics of transmission medium
Signal levels
Data rates
Unit-1

## Slide 18: Network Access/Data Link layer(1)
Data Link Control(Logical Link Control) Sub Layer
  Means of activating, maintaining and deactivating
  a reliable link
  Framing (Header)
  Error detection and control
Media Access Control (MAC) sub layer
  Allocation of channel
  Physical addressing (MAC address)
  Higher layers do not need to know about underlying technology
  Virtual point-point links between pair of stations
Unit-1

## Slide 19: IP Layer
Exchange of data between end system and network
Destination address provision
Systems may be attached to different networks
Datagram
Routing functions across multiple networks
Implemented in end systems and routers
Invoking services like priority
Connection less service
Fragmentation
Routing and IP addresses
ARP and RARP
Unit-1

## Slide 20: Transport Layer (TCP/UDP)
Connection-less and connection oriented service
Reliable delivery of data
Segments
Congestion control
Ordering of delivery(Reassembling)
  Architecture specific (Big-endian or Little-endian)
Addressing (Port no. or SAP)
UDP (TFTP, NFS, DNS)
TCP (SMTP, HTTP, FTP)
Error Control
Unit-1

## Slide 21: Application Layer
Support for user applications
File transfer
User applications
Reliable data transfer for UDP users
Network management
E.g. http, SMTP, FTP, etc.
Unit-1

## Slide 22: Internet protocol stack
Introduction
1-
application: supporting network applications
  FTP, SMTP, HTTP
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  PPP, Ethernet
physical: bits “on the wire”
application
transport
network
link
physical

## Slide 23: Encapsulation
Introduction
1-
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame

## Slide 24: Protocol Hierarchies (2)
Example information flow supporting virtual communication in layer 5.
Unit-1

## Slide 25
Thank You