## Slide 1: LECTURE 7 outline
3.1 Transport-layer services
3.2 Multiplexing and demultiplexing
3.3 Connectionless transport: UDP
Flow Control Techniques

## Slide 2: Transport services and protocols
provide logical communication between app processes running on different hosts
transport protocols run in end systems
  send side: breaks app messages into segments, passes to network layer
  rcv side: reassembles segments into messages, passes to app layer
more than one transport protocol available to apps
  Internet: TCP and UDP
application
transport
network
data link
physical
application
transport
network
data link
physical
logical end-end transport

## Slide 5: Transport vs. network layer
network layer: logical communication between hosts
transport layer: logical communication between processes
  relies on, enhances, network layer services
Household analogy:
12 kids sending letters to 12 kids
processes = kids
app messages = letters in envelopes
hosts = houses
transport protocol = Ann and Bill
network-layer protocol
= postal service

## Slide 6: Internet transport-layer protocols
reliable, in-order delivery (TCP)
  congestion control
  flow control
  connection setup
unreliable, unordered delivery: UDP
  no-frills extension of “best-effort” IP
services not available:
  delay guarantees
  bandwidth guarantees
application
transport
network
data link
physical
network
data link physical
network
data link physical
network
data link physical
data link
physical
network
data link
physicalnetwork
network
data link physical
application
transport
network
data link
physical
logical end-end transport

## Slide 7: Chapter 3 outline
3.1 Transport-layer services
3.2 Multiplexing and demultiplexing
3.3 Connectionless transport: UDP
3.4 Principles of reliable data transfer
3.5 Connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 Principles of congestion control
3.7 TCP congestion control

## Slide 8: Multiplexing/demultiplexing
application
transport
network
link
physical
P1
application
transport
network
link
physical
application
transport
network
link
physical
P2
P3
P4
P1
host 1
host 2
host 3
= process
= socket
delivering received segments to correct socket
Demultiplexing at rcv host:
gathering data from multiple sockets, enveloping data with header (later used for demultiplexing)
Multiplexing at send host:

## Slide 9: Chapter 3 outline
3.1 Transport-layer services
3.2 Multiplexing and demultiplexing
3.3 Connectionless transport: UDP
3.4 Principles of reliable data transfer
3.5 Connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 Principles of congestion control
3.7 TCP congestion control

## Slide 10: UDP: User Datagram Protocol [RFC 768]
“no frills,” “bare bones” Internet transport protocol
“best effort” service, UDP segments may be:
  lost
  delivered out of order to app
connectionless:
  no handshaking between UDP sender, receiver
  each UDP segment handled independently of others
Why is there a UDP?
no connection establishment (which can add delay)
simple: no connection state at sender, receiver
small segment header
no congestion control: UDP can blast away as fast as desired

## Slide 11: UDP: more
often used for streaming multimedia apps
  loss tolerant
rate sensitive
other UDP uses
  DNS
  SNMP
reliable transfer over UDP: add reliability at application layer
  application-specific error recovery!
source port #
dest port #
32 bits
Application data (message)
UDP segment format
length
checksum
Length, in
bytes of UDP
segment, including header

## Slide 12: UDP checksum
Sender:
treat segment contents as sequence of 16-bit integers
checksum: addition (1’s complement sum) of segment contents
sender puts checksum value into UDP checksum field
Receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  NO - error detected
  YES - no error detected. But maybe errors nonetheless? More later
….
Goal: detect “errors” (e.g., flipped bits) in transmitted segment

## Slide 13: Flow Control
In computer networks, flow control is defined as - A set of procedures which are used for restricting the amount of data that a sender can send to the receiver.
Flow Control Protocols-

## Slide 14: Stop and Wait Protocol-
Stop and Wait Protocol is the simplest flow control protocol.
It works under the following assumptions-
Communication channel is perfect.
No error occurs during transmission.
Working
Sender sends a data packet to the receiver.
Sender stops and waits for the acknowledgement for the sent packet from the receiver.
Receiver receives and processes the data packet.
Receiver sends an acknowledgement to the sender.
After receiving the acknowledgement, sender sends the next data packet to the receiver.

## Slide 16
Total time taken in sending one data packet
= (Transmission delay + Propagation delay + Queuing delay + Processing delay)packet
+
(Transmission delay + Propagation delay + Queuing delay + Processing delay)ACK
Assume Queuing delay and processing delay to be zero at both sender and receiver side.
Transmission time for the acknowledgement to be zero since it’s size is very small.
Under the above assumptions.
Total time taken in sending one data packet
= (Transmission delay + Propagation delay)packet + (Propagation delay)ACKWe know,
Propagation delay depends on the distance and speed. So, it would be same for both data packet and acknowledgement.
So, we have-
Total time taken in sending one data packet
= (Transmission delay)packet + 2 x Propagation delay

## Slide 17: Efficiency-
Efficiency of any flow control control protocol is given by-
Efficiency (η) = Useful Time / Total Time
where-
Useful time = Transmission delay of data packet = (Transmission delay)packet
Useless time = Time for which sender is forced to wait and do nothing = 2 x Propagation delay
Total time = Useful time + Useless time