## Slide 1
LECTURE : 18B11CS311PML02
PROGRAMME : B.Tech.
COURSE TITLE : Computer Network and IoT
LECTURE TITLE : CIRCUIT SWITCHING AND PACKET SWITCHING , Physical Media
FACULTY NAME : Mr. Pankaj Mishra

## Slide 2
By
Mr. Pankaj Mishra Dept. of CSE & IT JIIT, NOIDA
CIRCUIT SWITCHING AND PACKET SWITCHING , Physical Media

## Slide 3
Circuit Switching
Packet Switching
Physical Media
Topics of Today’s Lecture

## Slide 4: Circuit Switching
Introduction
1-
Circuit switching is a communication method where a dedicated communication path, or circuit, is established between two devices before data transmission begins. The circuit remains dedicated to the communication for the duration of the session, and no other devices can use it while the session is in progress. Circuit switching is commonly used in voice communication and some types of data communication.

## Slide 5: Circuit Switching: FDM and TDM
Introduction
1-
FDM
frequency
time
TDM
frequency
time
4 users
Example:
Notes: Two simple multiple access control techniques.
Each mobile’s share of the bandwidth is divided into portions for the uplink and the downlink. Also, possibly, out of band signaling.
As we will see, used in AMPS, GSM, IS-54/136

## Slide 6: Numerical example
Introduction
1-
How long does it take to send a file of 640,000 bits from host A to host B over a circuit-switched network?
  All links are 1.536 Mbps
  Each link uses TDM with 24 slots/sec
  500 msec to establish end-to-end circuit
Let’s work it out!

## Slide 10
Packet Switching

## Slide 11: store-and-forward
Introduction
1-
Takes L/R seconds to transmit (push out) packet of L bits on to link or R bps
Entire packet must arrive at router before it can be transmitted on next link: store and forward
delay = 3L/R (assuming zero propagation delay)
Example:
L = 7.5 Mbits
R = 1.5 Mbps
delay = 15 sec
R
R
R
L
more on delay shortly …

## Slide 12: Physical Media
Introduction
1-
Bit: propagates between transmitter/rcvr pairs
physical link: what lies between transmitter & receiver
guided media:
  signals propagate in solid media: copper, fiber, coax
unguided media:
  signals propagate freely, e.g., radio
Twisted Pair (TP)
two insulated copper wires
  Category 3: traditional phone wires, 10 Mbps Ethernet
  Category 5: 100Mbps Ethernet

## Slide 13: Physical Media: coax, fiber
Introduction
1-
Coaxial cable:
two concentric copper conductors
bidirectional
baseband:
  single channel on cable
  legacy Ethernet
broadband:
  multiple channels on cable
  HFC
Fiber optic cable:
glass fiber carrying light pulses, each pulse a bit
high-speed operation:
  high-speed point-to-point transmission (e.g., 10’s-100’s Gps)
low error rate: repeaters spaced far apart ; immune to electromagnetic noise

## Slide 14: Physical media: radio
Introduction
1-
signal carried in electromagnetic spectrum
no physical “wire”
bidirectional
propagation environment effects:
  reflection
  obstruction by objects
  interference
Radio link types:
terrestrial microwave
  e.g. up to 45 Mbps channels
LAN (e.g., Wifi)
  11Mbps, 54 Mbps
wide-area (e.g., cellular)
  e.g. 3G: hundreds of kbps
satellite
  Kbps to 45Mbps channel (or multiple smaller channels)
  270 msec end-end delay
  geosynchronous versus low altitude

## Slide 15
Thank You